# Project Part 3
James Gaul
Andy Eslick
## Introduction
During this semester, we created three processors that implement the RISC-V ISA using three different implementation strategies: Single Cycle, Software Scheduled Pipeline, and Hardware Scheduled Pipeline. For each processor, we sketched a high level design, implemented the processor, wrote tests, debugged, and did performance analysis after the processor was confirmed to be working.
## Benchmarking
Single / Cycle	Instruction Count	Total Cycles to execute	CPI	Maximum Cycle Time	Total Execution Time
Testbench	115	115	1.0	36.27 ns	4 171.05 ns
Grendel	2 129	2 129	1.0	36.27 ns	77 218.83 ns
Mergesort	549	549	1.0	36.27 ns	19 912.23 ns

Software Scheduled / Pipeline	Instruction Count	Total Cycles to execute	CPI	Maximum Cycle Time	Total Execution Time
Testbench				17.72 ns
Grendel	6 013	6275	1.04	17.72 ns	110 812.37 ns
Mergesort	1425	1515	1.06	17.72 ns	26 750.95 ns

Hardware Scheduled / Pipeline	Instruction Count	Total Cycles to execute	CPI	Maximum Cycle Time	Total Execution Time
Testbench	115	214	1.86	19.42 ns	4 153.93 ns
Grendel	2 129	7073	3.32	19.42 ns	137 265.99 ns
Mergesort	549	1551	2.83	19.42 ns	30 172.27 ns

## Performance Analysis
"Instruction Count" times "CPI" times "Maximum Cycle Time" gives us our total execution time in nanoseconds. For each processor, we synthesized it to get our Maximum Cycle Time, and ran each test program (Testbench, Grendel, and Mergesort) using the provided toolflow to get the instruction count from RARS, the cycle count, and CPI.
Each processor has its own pros and cons, come of which are detailed below.
	Single Cycle	Software Scheduled	Hardware Scheduled
Pros	No hazards / Small instruction count	No hazard detection overhead / Small cycle time	Small Instruction Count / Register Forwarding / Small cycle time
Cons	Large cycle time	Large instruction count / No forwarding	Hazard detection overhead

## Software Optimization
## Hardware Optimization
For our Software Scheduled pipeline, the slowest stage was Execute (, with the ALU Control taking around 3 ns, and the ALU’s AddSub module taking around 13 ns to complete. ALU Control only needs the current instruction to set the signals for the ALU. If we moved the ALU Control to the Instruction Decode stage, we could bring the cycle time for Execute down from
On our hardware scheduled pipeline, the Hazard Detection Unit contributed about 4 ns to each cycle, making up ~20% of the overall cycle time to each cycle. The time is split between decoding the instruction in IF, and actually sending the signals for avoiding hazards. Within the Hazard Detection Unit, 2 ns was spent comprehensively extracting fields (RS1, RS2, RD, Instruction Encoding, etc.) from each instruction stage in parallel. If we cut down on the number of fields extracted from each instruction, we would make the Hazard Detection Unit faster, and lower the maximum cycle time.
## It Depends
## Challenges
## Demo